Water Use Monitor Project Notes
Jesse Millwood
Project Assigned: 2014 January 6th

Project Description:

The Water Use Monitor is meant to be a device with a character display that can be mounted or sit on top of the Board-Washer. The device will monitor the usage of water in two separate locations that can be individually reset . The two water usage statistics are meant to correspond to the amount of water that has been run through the water treatment tanks that treat the water feeding into the Board-Washer. These chemicals run out at different water usage quantities. The amount of water for one wash cycle should also me measured so that the number of cycles may be estimated and displayed as well.

Interface Ideas:

  Water Usage Monitor
        Cycles / gallons
  → Tank 1 : 0000 / 0000
       Tank 2: 0000 / 0000

Rotary Highlight / Select

Power LED

Reset Tactile Switch
Status RGB

Interface Idea 1:
2014 January 6th
- Rotary encoder with Built in Tactile Button
- One Reset tactile button
- Status RGB LED
- Power LED

The user would highlight which chemical tank properties to edit with a the rotary encoder. The choices would be Tank1, Tank1 cycles, Tank1 gallons, and same for Tank 2. If Tank 1 or Tank 2 are highlighted and the select button is pushed, the user can reset the count by pressing the reset button. If the cycles or gallon count is highlighted for either tank and the select button is pressed the user will be able to manually set the desired parameter to the desired quantity by rotating the rotary encoder. The quantity will be locked in by pressing the rotary encoder again. The device will store parameters in EEPROM so if one parameter or both parameters were reset on accident, the user can hold the reset button for 3 seconds and release and the previous quantities will be displayed again. The Status RGB LED will be lit blue in stand by, green while a cycle is in progress, yellow when there there are less than 5 wash cycles left for one of the tanks, and red when one of the tanks needs to be changed and the counter reset.

MCU I/O Considerations:
- 11 pins – (Could use 02 pins for I2C version) 8bit 4x20 Character Display
- 01 pins – Reset Tactile Switch
- 03 pins – (could use on-semi 5623 and i2c, just 02 pins) RGB LED
- 03 pins – (02 INT pins for the rotation sensing) Rotary Encoder
- 01 pins – (ICP1 pin used for Input Capture Pin)Flow Sensing

Total Pin Usage:
- 19 pins Without I2C
- 09 pins With I2C
Available IO Pins:
- ATmega328P:	23 Max IO Pins
- ATtiny84A:	12 Max IO Pins

Interface Idea 2:
2014 January 7th

Ryan advised not to use the I2C for the display or the RGB LED driver. He also mentioned using the ATmega48/88 as the MCU.

Parts:
Character Display : NewHaven 4x20 Char. Display DIGI: NHD-0420H1Z-FL-GBW-33V3-ND
Micro-controller : Most Likely Will Use ATmega168A DIGI: ATMEGA168PA-AURCT-ND
Case : SL-series : http://www.polycase.com/sl-64p#
Tactile Switch Buttons : TE Connectivity PN: 2-1825955-6 (13mm actuator Height from board)
DIGI: 450-1641-ND
Rotary Encoder/Tactile SW: TE Connectivity PN: EN11-HSB1AF15
Matching Knob: DIGI- 226-4092-ND
RGB LED: 5mm DIGI T-1 Part no: 754-1615-ND (Not using RGB, Just regullar 5mm LEDS)
Status LED: 5mm T-1 3/4 DIGI Part no: Green 516-1347-ND
Power LED: 5mm T-13/4 DIGI Part no: Red 365-1189-ND
SMT Potentiometer for Contrast adjustment : Stock
Water Flow Sensor: Omega Engineering FTB4705 SN: 112013001141
Crystal: XC1291CT-ND
POWER:
LDO: LT1763CS8#PBF-ND
LDO: (STOCK): Stock +3V3 LDO used instead of a 5.5V ldo because can use the 5V wall wart and will not have to step anything down for the 5V line, which does not really need to be very clean

Wall Wart: 9V 1A switching, (90 deg con) DIGI-Key Number: T1019-P5RP-ND
Wall Wart: Stock 5V wall wart
Matching DC INPUT: Low profile jack Digi key part number: CP-051AH-ND
Decided to use DC INPUT: CP-002A-ND because it was longer and made it easier to interface from the board to the case wall

Look for ISP programmer header that is surface mount and low profile: 952-2121-ND
Room needed: 8.64 mm
Look for interface ideas for the sensor:
Board Side: WM4901-ND
Wire Side: WM6274-ND

Power Considerations:

- MCU:	1.8V-5.5V
- LED Character Display Logic:	3.3V
- LED Character Display LED:	3.0V
- Water Flow Sensor:	5.0V-30V	needs pullup from sensor to vcc

Part	Supply Voltage	Current
MCU IDLE	1.8V – 5.5V	2.7 mA
LED Character Display Logic	3.3V	4 mA
LED Character Display LED	3.0V	150 mA
RGB LED	1.9V(R), 3.3V(G), 3.3V(B)	20 mA
Status LED	2V	20 mA
Flow Sensor	5.0V – 30V	0.5 mA w/ 10kΩ pull-up

Part Height Considerations For Enclosure

Room available in Enclosure: 0.634”(middle - bottom), 0.653”(middle - top)

Part	Height
Power Jack	10.9 mm / 0.43 in
Sensor Jack	6.99 mm / 0.275 in
LCD Character Display	13 mm / 0.512 in
Encoder w/ Knob	23 mm /0.912 in
Tactile Switch	13mm / 0.512 in

Want Stand off from PCB mounts on bottom half of case: about 0.2035in , 5.1689mm
Stand off mounting hardware:
Spacer: 492-1074-ND
Screws: #4 x 3/8” screws (0.25” stand off and 0.25” allowable in case mounting hole )
DIGI: H800-ND , Have these in stock at 3/8 length and 1/2

Electric Protection
POWER: P-CH MOSFET(DMP2305U-7) with zener diode (BZX84-C5V1,215)
- Gate to resistor to ground
- Drain to source
- Zener : a-gate, c-source
- Source to load
PIN: